## Slide 1: Chapter 11
Learning Objectives:
Domain 4: Communication and Network Security
  4.1 Implement secure design principles in network architectures
    4.1.1 Open System Interconnection (OSI) and Transmission Control Protocol/Internet Protocol (TCP/IP) models
    4.1.2 Internet Protocol (IP) networking
    4.1.3 Implications of multilayer protocols
    4.1.4 Converged protocols
    4.1.5 Software-defined networks
    4.1.6 Wireless networks

## Slide 2: Chapter 11
Learning Objectives:
Domain 4: Communication and Network Security
  4.2 Secure network components
    4.2.1 Operation of hardware
    4.2.2 Transmission media
    4.2.3 Network Access Control (NAC) devices
    4.2.4 Endpoint security
    4.2.5 Content-distribution networks

## Slide 3: History of the OSI Model
A protocol is asset of rules and restrictions that define how data is transmitted over a network medium
In the early 1970s, ISO developed the Open System Interconnection Model to standardize communication protocols; ISO 7498
Prior to the OSI model, DARPA developed the TCP/IP model
Just a reference model, but essential to the CISSP exam
  Serves as an abstract framework for how protocols should function in an ideal world on ideal hardware

## Slide 4: OSI Functionality
Divides networking tasks into seven distinct layers
It is an open network architecture guide for network product vendors
The real benefit of the OSI model is its expression of how networking actually function

## Slide 5: Encapsulation/De-encapsulation
Encapsulation is the addition of header, and possible a footer, to the data received each layer above before it’s hands off the layer below
The inverse process is called de-encapsulation

## Slide 6: OSI Layers
Physical Layer
Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer

## Slide 7: TCP/IP Model

## Slide 8: TCP/IP Protocol Suite Overview
Not just a single protocol, but a protocol stack comprising dozens of individual protocols
A platform-independent protocol based on open standards
TCP/IP can be secured using VPN links
  PPTP
  L2TP
  SSH
  OpenVPN
  IPsec

## Slide 9: Transport Layer Protocols
TCP – connection-oriented; full duplex protocol
UDP – connectionless; simplex protocol
Port numbers: 0 - 65,535
  Well-known ports: 0-1023
  Registered ports: 1024-49151
  Dynamic/Private/Random/Ephemeral ports: 49152-65535

## Slide 10: Transport Layer Protocols
3-way handshake:
  SYN
  SYN/ACK
  ACK
TCP header flags:
  Table 11.2 (page 456)

## Slide 11: Network Layer Protocols and IP Networking Basics
IPv4 vs IPv6
  IPv4 – 32 bit, dotted-decimal
  IPv6 – 128 bit, hexadecimal
IP classes
ICMP – ping, traceroute, pathping
IGMP - multicasting
ARP – IP  MAC mapping

## Slide 12: Common Application Layer Protocols
Telnet
FTP
TFTP
SMTP
POP3
IMAP4
DHCP
HTTP
SSL/TLS
Line Print Daemon
X Window
  GUI API for command-line OSs
Network File System
  File sharing between dissimilar systems
SNMPv3
Page 462 and 463

## Slide 13: Implications of Multilayer Protocols
TCP/IP is a multilayer protocol
Many benefits; encapsulation
Some not so nice benefits; encapsulation
  Encapsulating one protocol inside another could allow covert channels
  Unbounded encapsulation support; the ability to jump between VLANs; VLAN hopping
Distributed Network Protocol (DNP3) – primarily used in the electric and water utility and management industries; ICS and SCADA

## Slide 14: TCP/IP Vulnerabilities
Improperly implemented TCP/IP stacks in various OSs are vulnerable to buffer overflows, SYN flood attacks, DDoS attacks, fragment attacks, oversized packet attacks, spoofing attacks, man-in-the-middle attacks, hijack attacks, and coding attacks
Subject to passive monitoring attacks

## Slide 15: Domain Name System
Addressing and numbering
  MAC address – hardware address, physical address, Layer 2 address, permanent address
  IP address - logical address, “temporary” address
  Domain name – human-friendly name
Domain Name System and ARP were developed to interchange or resolve between domain names and IP addresses or IP addresses and MAC addresses
Three main parts:
  Top-level domain (TLD)
  Registered domain name
  Subdomain or hostname

## Slide 16: Domain Name System
The primary authoritative name server hosts the original zone file for the domain
The secondary authoritative name server can be used to host read-only copies for the zone file
DNS common resource records
  See page 467
Domain Name System Security Extension (DNSSEC)
  A security improvement to the existing DNS infrastructure
    Provide reliable authentication between devices during DNS operations
    Uses digital certificates to perform mutual authentication
    The goal is to prevent DNS abuses

## Slide 17: DNS Poisoning
Can take place at any of the steps involved in name resolution, but is easiest is to corrupt the HOSTS file or the DNS server query
Deploy a rogue DNS server
Perform DNS poisoning
Alter the HOSTS file
Corrupt the IP configuration
Use proxy falsification
Pharming; similar to DNS poisoning; redirect attack often through phishing attack

## Slide 18: Domain Hijacking
Aka domain theft
The malicious action of changing the registration of a domain name without the authorization of the valid owner
Accomplished through stealing login credentials, using XSRF, hijacking a session, using MitM or exploiting a flaw in the domain registrar’s system

## Slide 19: Converged Protocols
Merging of specialty or proprietary protocols with standard protocols such as those from TCP/IP
Primary benefit: use existing TCP/IP supporting network infrastructure to host special or proprietary services without the need for unique deployments of alternate networking hardware.
Fibre Channel over Ethernet (FCoE)
Multiprotocol Label Switching (MPLS)
Internet Small Computer System Interface (iSCSI)
Voice over IP (VOIP)
Software-Defined Networking (SDN)

## Slide 20: Content Distributed Networks
Content Distributed Network or Content Delivery Network
  A collection of resource services deployed in numerous data centers across the Internet in order to provide low latency, high performance, and high availability of hosted content
  Provide desired multimedia performance quality demanded by customers through the concept of distributed data hosts
  Results in a type of geographical load-balancing
  Examples: CloudFare, Akamai, Amazon CloudFront, CacheFly, and Level 3 Communications

## Slide 21: Wireless Networks
Securing Wireless Access Points
  Adjust power settings
  Infrastructure mode
Securing the SSID
  Disable the beacon frame for the SSID; but can still be detected
  Use WPA2
Conducting a Site Survey
Using Security Encryption Protocols
  WEP
  WPS
  WPA
  WPA2

## Slide 22: Wireless Networks
Using Security Encryption Protocols
  WEP
  WPS
  WPA
  WPA2
  802.1X/EAP
    PEAP
    LEAP
  MAC Filter
  TKIP
  CCMP

## Slide 23: Wireless Encryption Standards
 |  | Authentication | Encryption | Integrity | Standard
WEP |  | Pre-Shared Key (PSK) | 24-bit I.V. + 40-bit key RC-4 cipher | CRC32 | 802.11
WPS |  | Push-button | 24-bit I.V. + 40-bit key RC-4 cipher | CRC32 | 802.11
 |  | PIN |  |  | 
WPA | Personal | PSK | 48-bit I.V + PSK =128-bit key RC-4 | TKIP (MIC) | 802.11i
 | Enterprise | 802.1X |  |  | 
WPA2 | Personal | PSK | 48-bit I.V. + PSK = 256-bit key AES-CCMP | CBC-MAC | 802.11i
 | Enterprise | 802.1X |  |  | 

## Slide 24: Determining Antenna Placement
Guidelines:
  Use a central location
  Avoid solid physical obstructions
  Avoid reflective or other flat metal surfaces
  Avoid electrical equipment
Antenna types
  Omnidirectional
    Base antenna or “rubber duck”
  Directional
    Yagi, cantenna, panel, and parabolic
Adjusting power levels
  When adjusting power levels, make minor adjustments
  After each adjustment, reboot the WAP before performing another site survey

## Slide 25: WPS
A security standard for wireless network
Simplifies the effort involved in adding new clients to a well-secured wireless network
Push-button or PIN access methods
Susceptible to brute-force attacks

## Slide 26: Using Captive Portals
Redirects newly connected wireless web clients to a portal access control page
May require the user to input payment information, provide logon credentials, or input an access code
Also used to display acceptable use policy, privacy policy, and tracking policy to the user
Often used at hotels, restaurants, bars, airports, libraries, education centers, etc.

## Slide 27: General Wi-Fi Security Procedure
Change the default administrator password
Enable or disable SSID broadcast
Change the SSID to something unique
Enable MAC filtering
Consider static IP addresses
Use the strongest authentication and encryption
Treat wireless as remote access and separate using a firewall
Requires all transmission between wireless clients and WAPs to be encrypted

## Slide 28: Wireless Attacks
War Driving
War Chalking
Replay
IV
Rogue Access Points
Evil Twin

## Slide 29: Secure Network Components
Intranet – a private network designed to host the same information services found on the internet
Extranet – a cross between the internet and an intranet; a section of the organization’s network that has been sectioned off so that I acts as and intranet for the private network but also serves information to the public internet; often reserved for specific customers
  A DMZ is a public extranet
Network Segmentation can:
  Boosting performance
  Reducing Communications Problems
  Provide Security

## Slide 30: Network Access Control
NAC is concept of controlling access to an environment through strict adherence to and implementation of security policy
Goals:
  Prevent/reduce zero-day attacks
  Enforce security policy throughout the network
  Use identities to perform access control
Goals can be achieved through the use of strong detailed security policies that define all aspects of security control, filtering, prevention, detection, and response for every device from client to server and for internal or external communication
Acts as an automated detection and response system
Can be implemented with a preadmission philosophy or a post admission philosophy or both

## Slide 31: Firewalls
Firewalls are essential tools in managing and controlling network traffic
Typically deployed between a private network and a link to the internet, but can deployed between departments within an organization
Filters traffic based on a set of rules or access control lists
Blocks or filters traffic, but does not block viruses or malicious code transmitted through authorized connections
Only one part of overall security solution

## Slide 32: Firewalls
Several types of firewalls:
  Static Packet-Filter Firewalls
    Examines data from a message header
    First generation firewalls
  Application-Level Gateway Firewalls
    Also called a proxy firewall; filters traffic based on the internet service
    Second generation firewalls
  Circuit-level Gateway Firewalls
    Establish communication sessions between trusted partners
    Manage communications based on the circuit, not the content
    Second generation firewalls
  Stateful Inspection Firewalls
    Dynamic packet filtering firewalls; evaluate the state or context of the traffic
    Able to grant a broad range of access for authorized users and activities
    Third generation firewalls
  Deep Packet Inspection Firewalls
    Filtering mechanism that operates typically at the Application Layer; filters content rather than header
  Next-Generation Firewalls
    Composed of several features in addition to a firewall; IDS/IPS, SSL/TLS proxy, web filtering, QoS management bandwidth throttling, NAT, VPN gateway, and antivirus

## Slide 33: Multihomed Firewalls
Some firewalls have more than one interface
A bastion host is a computer or appliance that is exposed on the internet and has been hardened by removing all unnecessary elements
A screened host is a firewall-protected system logically positioned just inside a private network; screens traffic inbound to the network and protects the identity of internal clients

## Slide 34: Firewall Deployment Architectures
Single-tier
  Useful against generic attacks; offers minimal protection
Two-tier
  Two different designs
    One uses a firewall with three or more interfaces and separates private network from the DMZ using interfaces
    The second uses two firewalls in series allowing public accessibility
Three-tier
  Deployment of multiple subnets between the private network and the internet separated by firewalls
  The outer subnet is usually a DMZ; the middle subnet can server as a transaction subnet; the third subnet can support the private network
  See page 491

## Slide 35: Endpoint Security
The concept that each individual device must maintain local security whether or not its network or telecommunication channels also provide or offer security
Traditional security depended on network border sentries
  Firewalls, proxies, centralized virus scanner, and IDS/IPS
This is no longer considered best business practice
  Firewalls, proxies, centralized virus scanner, and IDS/IPS
End point security should be viewed a an aspect of the effort to provide sufficient security on each individual host

## Slide 36: Secure Operation of Hardware
Repeaters, Concentrators, and Amplifiers – Layer 1 devices
Hubs – Layer 1
Modems – traditional landline modems
Bridges – Layer 2; connects two networks; store-and-forward device
Switches – Layer 2; directs traffic directly to host based on MAC address
Routers – Layer 3; routes traffic based on IP address; routing protocols
Brouters – combination device of router and bridge; attempts to route first, then defaults to bridging
Gateways – connects networks that are using different network protocols; responsible for transferring traffic from one network to another by transforming the format of that traffic
Proxies – serves as mediators, filters, caching servers and NAT/PAT servers
LAN extenders – remote access, multilayer switch used to connect distant network over WAN links

## Slide 37: Cabling, Wireless, Topology, Communications, and Transmission Media Technology
Transmission Media
Coaxial Cable (coax)
  Internal; 10Base2 and 10Base5
  External; broadband cable
Baseband and Broadband Cables
  Baseband: transmits only a single signal at a time
  Broadband: transmit multiple signals simultaneously
Twisted Pair
  UTP
  STP
Conductors
  Copper is resistant to the flow of electrons; results in degradation of the signal strength and quality over the length of the cable

## Slide 38: Network Topologies
Ring Topology
  Connects clients or nodes in a ring fashion
  Token based; 802.5 (Token Ring)
Bus Topology
  Connects each nodes to a trunk or backbone cable
  Prone to collisions (CSMA/CD)
  Two types: linear and tree (page 502)
Star Topology
  Employs a centralized connection device
  Generally, a central hub or switch is a SPOF
  Physical topology and logical topology do not have to match
Mesh Topology
  Connects systems to other system using numerous path
    Full
    Partial

## Slide 39: Wireless Communications and Security
General Wireless Concept
  Transmits data over radio frequencies
  900 MHz, 2.4 GHz, and 5 GHz
  Frequency Hopping Spread Spectrum (FHSS) – transmits data in a series while constantly changing the frequency
  Direct Sequence Spread Spectrum (DSSS) – employs all the available frequencies simultaneously
  Orthogonal Frequency-Division Multiplexing (OFDM) – employs a digital multicarrier modulation scheme

## Slide 40: Cell Phones
Phones connect to cell towers and directs calls based on telecommunications carriers infrastructure
Not all cell phone traffic is voice
Communications over a cell phone provider’s network are not necessarily secure

## Slide 41: Bluetooth (802.15)
Personal Area Network (PAN)
2.4 GHz
Pairing
Bluejacking – usually one-way hacking; sending data only
Bluesnarfing – two-way hacking; stealing data
Bluebugging – grants hackers remote control over the feature and functions of a Bluetooth device
Limited range: 30 feet typically
Encryption, if implemented, is weak

## Slide 42: RFID
Radio Frequency Identification
  Tracking technology based on the ability to power a radio transmitter using current generated in an antenna when place in a magnetic field
  Allow for quick inventory tracking without having to be in direct physical proximity of the device; RFID reader
  Stealing data via a RFID reader

## Slide 43: NFC
Near-field communications
  A standard that establishes short-range radio communications between device in close proximity
  A derivative of RFID technology
  Commonly found in mobile devices for data-to-data exchange
  Subjects to MitM attacks, eavesdropping, data manipulation, and replay attacks

## Slide 44: Phones
Cordless phones
  900 MHz, 2.4 GHz, or 5 GHz
  Handset transmits to a base station via RF signals
Mobile Devices
  Smartphones and other devices present an ever-increasing security risk
  Support memory cards and USB connections
  Loss or theft of a mobile device could mean compromise of personal and/or corporate secrets
  Keep nonessential information off the portable device
  Not immune to eavesdropping; Stingray

## Slide 45: LAN Technologies
Ethernet
  Shared-media LAN technology
  Broadcast and collision domains
  Supports full-duplex using twisted-pair cable
  IEEE 802.3
Token Ring
  Employs a token-passing technology to control which system can transmit data
  Rarely used today due to performance limitations, higher cost compared to Ethernet, and increased difficulty in deployment and management
  Multistation Access Unit
FDDI
  High-speed token-passing technology that employs two fiber optic rings
  Self-healing; expensive

## Slide 46: Sub technologies
Analog and Digital
Synchronous and Asynchronous
Baseband and Broadband
Broadcast, Multicast, and Unicast

## Slide 47: LAN Media Access
CSMA
  Does not address collisions
CSMA/CA
  AppleTalk and 802.11
  Request-to-Send/Clear-to-Send packets
  Attempts to avoid collisions
CSMA/CD
  Ethernet
  Responds to collisions
    Token Passing – performs communications using a digital token; FDDI and Token Ring
    Polling – performs communications using a master-slave configuration
      Primary system polls each secondary system in turn whether they have a need to transmit data
      Synchronous Data Link Control (SDLC)
      Attempts to reduce collision using a permission system

## Slide 48: Summary
Designing, deploying, and maintaining security on a network requires intimate knowledge about networking
OSI model vs TCP/IP model
Networking equipment
Converged protocols; FCoE, MPLS, VOIP, and iSCSI
Wireless communications; cell phone, Bluetooth, RFID, NFC, and 802.11