## Slide 1: Chapter 12
Learning Objectives:
Domain 4: Communication and Network Security
  4.3 Implement secure communication channels according to design
    4.3.1 Voice
    4.3.2 Multimedia collaboration
    4.3.3 Remote access
    4.3.4 Data Communications
    4.3.5 Virtualized networks

## Slide 2: Network and Protocol Security Mechanisms
Secure Communications Protocols
  IPsec
  Kerberos
  SSH
  Signal Protocol
  Secure Remote Procedure Call (S-RPC)
  SSL
  TLS

## Slide 3: Authentication Protocols
CHAP
PAP
EAP

## Slide 4: Secure Voice Communications
When voice communications occur over the IT infrastructure, it is important to implement mechanism to provide authentication and integrity
Confidentiality should be maintained by employing an encryption service or protocol to protect voice communications while in transit
PBX or POTS voice communications are vulnerable to interception, eavesdropping, tapping, and other exploitations
Physical security is required to maintain control over voice communications in the confines of your organization

## Slide 5: Voice over Internet Protocol (VOIP)
VOIP encapsulates audio into IP packets
It is important to keep security in mind when selecting a VOIP solution
  Caller ID and be falsified
  The call manager systems and VOIP phones themselves might be vulnerable to OS attack and DoS attacks
  Man-in-the-Middle attacks
  Deploying VOIP phones on the same switches a desktop and server systems
  Possible to listen to VOIP communications by decoding VOIP traffic
Secure Real-Time Transport Protocol
  Secure alternative to RTP and provides robust encryption and authentication

## Slide 6: Social Engineering
Gaining trust of employees through phone conversations
People within an organization make it vulnerable to social engineering attacks
Just a little information makes it possible to get a victim to disclose confidential information or engage in irresponsible activity
The only way to protect against social engineering is to teach users how to respond and interact with any form of communications
  Always err on the side of caution when voice communications is out of place
  Always request proof of identity
  Require callback authorizations on all voice-only requests
  Classify information and clearly indicate which information can be discussed or even confirmed using voice communications
  Ask why the information is needed an verify the identity again
  Never give out passwords via voice-only communications
  When disposing of office documentation, use secure disposal process, especially regarding IT infrastructure or its security mechanisms

## Slide 7: Fraud and Abuse
Private Branch Exchanges are susceptible to fraud and abuse
Phreakers may be able to gain unauthorized access to personal voice mailboxes, redirect messages, block access, and redirect inbound and outbound calls
Countermeasures:
  Consider replacing remote access or long-distance calling through the PBX with a credit card or calling card system
  Restrict dial-in or dial-out features
  For dial-in modems, use unpublished phone numbers outside of the prefix block range for your voice numbers
  Protect administrative interfaces for the PBX
  Block or disable any unassigned access codes or accounts

## Slide 8: Fraud and Abuse
Countermeasures (cont.):
  Define AUP and train users on how to properly use the system
  Log and audit all activities
  Disable maintenance modems and/or any form of remote administrative features
  Change all default configurations
  Block remote calling
  Deploy Direct Inward System Access (DISA) technologies to reduce PBX fraud by external parties; must be properly installed, configured, and monitored in order to obtain the desired security improvements
  Keep the system current with vendor updates

## Slide 9: Fraud and Abuse
Phreaker tools
  Black boxes are used to manipulate line voltages to steal long-distance services
  Red boxes are used to simulate tones of coins being deposited into pay phone
  Blue boxes are used to simulate 2600 Hz tones to interact directly with telephone network trunk systems
  White boxes are used to control the phone system; dual-tone multi-frequency (DTMF) generator (keypad); custom built or pieces of equipment most telephone repair personnel use

## Slide 10: Multimedia Collaboration
Remote Meeting
  Any product, hardware, or software that allows for interactions between remote parties
    Digital collaboration, virtual meetings, videoconferencing, software or application collaboration, shared whiteboard service, virtual training solutions, etc..
    Attendant security implementations must be evaluated
Instant Messaging
  Mechanisms that allows for real-time text-based chat between users locate anywhere on the internet
  Some IM utilities allow for file transfer, multimedia, voice and videoconferencing, and more
  Some are peer-to-peer; others are centralized
  Many forms of IM lack common security features, such as encryption

## Slide 11: Manage Email Security
Email infrastructure primarily consists of using
  Simple Mail Transfer Protocol (port 25)
    Designed to be a mail relay system
    Avoid open relay; does not authenticate senders before accepting and relaying mail; prime target for spammers
    Another option; SaaS email solutions; cloud-based email which provide high-availability, distributed architecture, ease of access, standardized configuration, and physical location independence
    Risks of cloud-based email services: blacklisting issues, rate limiting, app/add-on restriction and additional security mechanism you can deploy
  Post Office Protocol (port 110)
  Internet Message Access Protocol (port 143)

## Slide 12: Email Security Goals
Email in inherently not secure, but security can be added to email
  Provide for nonrepudiation
  Restrict access to messages to the intended recipients
  Authenticate and verify the source of message
  Verify the delivery of message
  Classify sensitive content within or attached to messages
Within the security policy
  Acceptable use policies for email
  Access control
  Privacy
  Email management
  Email backup and retention policies

## Slide 13: Understand Email Security Issues
The first step in deploying email security is to recognize the vulnerabilities specific to email
  SMTP, POP, and IMAP are not natively secure
Email is a common deliver mechanism for viruses, worms, Trojan horses, document with destruction macros, and other malicious code
Email offers little in the way of source verification possible to deliver email directly to user’s inbox on an email server by directly connecting to the email server’s SMTP port.
Email can be used as an attack mechanism; mail-bombing
Unwanted email can be considered an attack; spamming

## Slide 14: Email Security Solutions
Secure Multipurpose Internet Mail Extension (S/MIME)
  An email security standard that offers authentication and confidentiality to email through public key encryptions an digital signatures
  Signed vs enveloped message (page 533)
MIME Object Security Services (MOSS)
  Can provide authentication, confidentiality, integrity, and nonrepudiation for email
  Employs MD2 and MD5; RSA public key and DES to provide authentication and encryption
Privacy Enhanced Mail (PEM)
  An email encryption mechanism; uses RSA, DES, and X.509
Domain Keys Identified Mail (DKIM)
  A means to asset that valid mail is sent by an organization through verification of domain name identity
Pretty Good Privacy (PGP)
  Public-private key system that uses a variety of encryption algorithms to encrypt files and email message
  Open-source; OpenPGP and GPG
Opportunistic TLS for SMTP Gateways
  SMTP over TLS
Sender Policy Frameworks
  Protects against spam and email spoofing; operates by checking that inbound message originate from a host authorized to send message by the owners of the SMTP origin domain

## Slide 15: Email Security Solutions
Blocking attachments at the email gateway system eases the threats from malicious attachment
Blacklist services offer a subscription system to a list of known email abuse sources
Unwanted emails can be managed through the use of email reputation filtering
Fax security
  Fax encryptions, link encryption activity logs, and exception report
  Disable automatic printing
  Avoid fax machines that retain a copy of fax in memory or on a local storage device
  Fax to email instead of printing the documents

## Slide 16: Remote Access Security Management
Telecommuting has become a common feature for business computing
Usually requires remote access
  Using a modem to dial up directly to a RAS
  Connecting to a network over the internet through a VPN
  Connecting to a terminal server system through a thin-client connection
  Connecting to an office-located personal computer using a remote desktop service
  Using cloud-based desktop solution

## Slide 17: Remote Access Security Management
When remote access capabilities are deployed in any environment, security must be considered and implemented to provide protection for your private network against remote access complications
  Remote access user should be stringently authenticated before being granted access
  Only those users who specifically need remote access for the assigned work tasks should be granted permission to establish remote connections
  All remote communications should be protected from interception and eavesdropping

## Slide 18: Plan Remote Access Security
Remote access security management strategy:
  Remote Connectivity Technology
    Each connection has its own unique security issues
  Transmission Protection
    VPNs, SSL/TLS, SSH, IPsec, L2TP
  Authentication Protection
    PAP, CHAP, EAP, RADIUS, TACACS+
  Remote User Assistance
    Technical assistance for users
Remote connections should be tightly controlled
Restrict remote access to only authorized users; use callback and caller ID

## Slide 19: Dial-up Protocols
A protocol must govern how the link is established
  Point-to-point Protocol (PPP)
    Full-duplex protocol used for transmitting TCPIP packet over various non-LAN connections; modems, ISDN, VPNs, Frame Relay, etc.
    Widely supported; authentication is protected using CHAP and PAP
    Replacement for SLIP and can support any LAN protocol
  Serial Line Internet Protocol (SLIP)
    Older technology developed to support TCP/IP over asynchronous connections
    Rarely used but still supported on many systems

## Slide 20: Centralized Remote Authentication Services
Remote Authentication Dial-In User Service (RADIUS)
  Centralized authentication for remote dial-up connections
  UDP over port 1812/1813
  TLS using TCP over port 2083 (Diameter)
Terminal Access Controller Access-Control System
  Alternative to RADIUS
  Port 49
  Three versions:
    Original TACACS – integrates the authentication and authorization process
    XTACACS – separates AAA
    TACACS+ - same as XTACACS, but adds two-factor authentication

## Slide 21: Virtual Private Networks
  Provides point-to-point transmission of both authentication and data traffic over an intermediary untrusted network
  Most use encryption to protect the encapsulated traffic
  Most commonly associated with establishing security communications paths through the internet
    Tunneling – process that protects the contents of protocol packets by encapsulating them in packets of another protocol
    How VPNs Work
      Can establish over any other network communications connection
      Can connect to individual systems or two entire networks

## Slide 22: Common VPN Protocols
Point-to-point Tunneling Protocol
  An encapsulation protocol developed from PPP
  Operates over Layer 2 of the OSI model
  Used on IP networks
  Protection includes; MS-CHAP, CHAP, PAP, EAP, SPAP (Shiva Password Authentication Protocol)
Layer 2 Forwarding Protocol and Layer 2 Tunneling Protocol
  Developed by Cisco
  Mutual authentication tunneling mechanism; no encryption
  Not widely deployed; replaced by L2TP
IP Security Protocol
  Both a standalone VPN protocol and the security mechanism for L2TP
  Can be used only for IP traffic
  Native in IPv6
  Two primary components:
    Authentication Header – Provides authentication, integrity, and nonrepudiation
    Encapsulating Security Payload (ESP) – provides encryption to protect the confidentiality of transmitted data, but can also perform limited authentication; operates at the Network Layer and can use either transport or tunnel mode

## Slide 23: Virtual LAN
Hardware-imposed network segmentation created by switches
  By default all ports are part of VLAN 1
Used for traffic management
communications between members of the same VLAN occur without hindrance
  But communications between VLANs requires routing functions
  Logically separate network without altering its physical topology
Easy to implement; little administrative overhead, and are a hardware-based solution
Controls and restricts broadcast traffic
Broadcast storm is a flood of unwanted Ethernet broadcast network traffic

## Slide 24: Virtualization
Used to host one or more operating systems within the memory of a single host computer
  Hosted OSs are called guest operating systems or instances
  Indistinguishable from traditional servers and services from the user’s perspective
Offers several benefits;
  Easier and faster to make backups of entire virtual systems
  Virtual systems can be replaced by a backup in minutes
  Malicious code compromise or infections of virtual systems rarely affect the host OS; allows for safe testing and experimentation

## Slide 25: Virtualization
VM escaping occurs when software within a guest OS is able to breach the isolation protection provided by the hypervisor in order to violate the container of other guest OSs or infiltrate the host OS
  VENOM exploit (page 547)
  Keep highly sensitive systems and data on separate physical machines
  Keep all hypervisor software current with vendor-released patches
  Monitor attack, exposure, and abuse indexes for new threats to your environment
Used for a wide variety of new architectures and system design solutions

## Slide 26: Virtual Software
Virtual application is a software product deployed in such a way that it is fooled into believing it is interacting the a full host OS
Virtual desktop refers to three different type of technology:
  A remote access tool that grants the users access to a distant computer system by allowing remote viewing and control of distant desktop’s display, keyboard, mouse, and so on
  An extension of the virtual application concept encapsulating multiple applications and some form of “desktop” or shell for portability or cross-OS operation
  An extended or expanded desktop larger than the display being used allows the user to employ multiple application layouts, switching between them using keystrokes or mouse movements

## Slide 27: Virtual Networking
The combination of hardware and software networking components into a single integrated entity
  Allows for software control over all network functions
  A single management console or interface can be used to oversee every aspect of the network
Software-defined networking (SDN) is unique approach to network operations design, and management
Based on the theory that complexities of a traditional network force organizations to stick with a single vendor
SDN aims at separating the infrastructure layer from the control layer
Removes the traditional networking concepts of IP addressing, subnets, routing, and the like from needing to be programmed into hosted devices
Offers a new network design that is directly programmable from a central location
Storage Area Network; a virtual SAN is a virtual re-creation of a SAN on top of a SDN

## Slide 28: Network Address Translation
The goal of hiding the identity of internal clients
A mechanism for converting internal IP addresses into public IP addresses
Developed to allow private network to use any IP address set without causing collisions or conflicts with public internet hosts
Benefits:
  Can connect an entire network to the internet using only a single or a few leased public IP addresses
  Can use the private IP addresses in a private network and still be able to communicate with the internet
  Hides the IP addressing scheme and network topography from the internet
  Restricts network connections so that only traffic stemming from connections originating from the internal protected network is allowed back into the network from the internet

## Slide 29: Private IP Addresses
NAT has proliferated because of the increased scarcity of public IPv4 addresses and security concerns
Private addresses:
All routers and traffic-filtering devices are configured by default to not forward private IP addresses
Class | Private IP range
A | 10.0.0.0 – 10.255.255.255
B | 172.16.0.0 – 172.31.255.255
C | 192.168.0.0 – 192.168.255.255

## Slide 30: Stateful NAT
NAT operates by maintaining a mapping between requests made by internal clients and the IP address of the internet service contacted
NAT can operate on a one-to-one basis with only a single client
  Can result in a bottleneck
Port address translation (PAT) aka NAT overloading
  Uses sockets; 192.168.1.3:80

## Slide 31: Static and Dynamic NAT
Static NAT
  Specific internal client’s IP address is assigned a permanent mapping to a specific external public IP address
Dynamic NAT
  Grants multiple internal clients access to a few leased public IP addresses
  The NAT system maintains a database of mapping so that all response traffic from internet services is properly routed to the original internal requesting client
  NAT is not directly compatible with IPsec because it modifies packet headers which IPsec relies on to prevent security violations
  However, there are versions of NAT proxies designed to support IPsec over NAT
    NAT-Traversal supports IPsec VPNs through the use of UDP encapsulation of IKE

## Slide 32: Automatic Private IP Addressing
APIPA assigns an IP address to a system in the event of DHCP assignment failure
Primarily a feature of Windows
  169.254.0.1 – 169.254.255.254
  Subnet mask of 255.255.0.0
  Can communicate with other APIPA clients but not any system across routers or with correctly assigned IP addresses
Loopback addresses
  The entire 127.x.x.x address range is set aside for testing the NIC’s TCP/IP protocol stack
  127.0.0.1 most commonly used

## Slide 33: Switching Technologies
Circuit Switching
  a dedicated physical pathway is created between the two communicating parties
  Once the call is established, the links remain the same throughout the conversation
  Once the path is disconnected, a different path is established if the two parties connect again
  Grants excusive use of the communications path to the current communication partners
Packet Switching
  Occurs when a message is broken up into small segments and send across the intermediary networks to the destination
  Each segment has its own header and takes any route to its destination
  Does not enforce exclusivity of communication pathways
Virtual Circuits
  A logical pathway or circuit created over a packet-switched network
    Permanent virtual circuit (PVC) – like a dedicated leased line; always exists; predefine circuit
    Switched virtual circuit (SVC) – more like a dial-up; assembled when needed, disassembled when not transmitting data

## Slide 34: WAN Technologies
WAN links can be divided onto two primary categories:
  Dedicated line (leased line) – indefinitely and continually reserved for use by a specific customer
    See page 556
  Nondedicated line – requires a connection to be established before data transmission can occur; can be used with any remote system that uses the same type of nondedicated line
    Standard modems
    DSL
    ISDN
      Basic Rate Interface: 2B+D; 144 Kbps
      Primary Rate Interface: 23B+D; 1.544 Mbps

## Slide 35: WAN Connection Technologies
X.25 WAN Connections
  Older packet-switching technology used in Europe
  Predecessor to Frame Relay; rarely used
Frame Relay Connections
  Packet-switching technology also uses PVCs
  Layer 2 connection
  Establishes virtual circuits between communications endpoints
  Cost is based on amount of data transferred
  Committed information rate (CIR)
  Requires the use of DTE/DCE at each connection point
Asynchronous transfer Mode (ATM)
  A cell-switching technology
  Fragments communications in 53-byte cells
  Very efficient; high throughputs
  Can be used with PVCs or SVCs
  connection-oriented packet-switching technology
  Older and being phased out

## Slide 36: WAN Connection Technologies
Switched Multimegabit Data Service (SMDS)
  Connectionless packet-switched technology
  Used to connect multiple LANs to form a MAN or a WAN
  Supports high-speed burst traffic and bandwidth on-demand
  Fragments into transmission cells
SDH and SONET
  fiber-optic high-speed networking standards
  SDH was standardized by the ITU; SONET standardized by the ANSI
  Mostly hardware or physical layer
  Synchronous time-division multiplexing to high-speed duplex communications
  Data rates (see page 560)
  Both support mesh and ring topologies

## Slide 37: Specialized Protocols
Synchronous Data Link Control (SDLC)
  Used on permanent physical connections of dedicated leased lines to provide connectivity for mainframes
High-Level Data Link Control (HDLC)
  A refined version of SDLC designed specifically for serial synchronous connections
  Support full-duplex communications and supports both point-to-point (PPP) and multipoint connections

## Slide 38: Dial-up Encapsulation Protocols
PPP is an encapsulation protocol designed to support the transmission of IP traffic over dial-up or point-to-point links
Allows for multivendor interoperability of WAN devices supporting serial links
Originally designed to support CHAP and PAP for authentication; however, recent versions of PPP also support MS-CHAP, EAP, and SPAP
Can also be used support internetwork Packet Exchange (IPX) and DECnet protocols
Replaced SLIP

## Slide 39: Miscellaneous Security Control Characteristics
Transparency
  The characteristic of a service, security control or access mechanism that ensures that it is unseen by users
  The more transparent a security mechanism is, the less likely a user will be able to circumvent it or be aware it exists
Verify Integrity
  use a checksum call a hash total
  Added to the end of a message
  When received the destination system performs a hash on the message and compares the digests
  Record sequence checking verifies packet or message sequence integrity
Transmission Mechanisms
  Transmission logging is a form of auditing focused on communications
  Transmission errors correction is a capability built-in to connection- or session-oriented protocols and services
  If a message was corrupted, altered, or lost, a request can be made to resend all or part of the message

## Slide 40: Security Boundaries
The line of intersection between an two areas, subnets, or environments that have different security requirements or needs
Exists between high-security area and a low-security area
  E.g., LAN and the internet
Security boundaries also exist between the physical environment and the logical environment
Security boundaries between protected and unprotected areas should always be clearly defined
It is important to state in a security policy the point at which controls end or begins and to identify that point in both the physical and logical environments
  Signs on a controlled access door that requires multi-factor authentication to gain access to a controlled access database

## Slide 41: Prevent or Mitigate Network Attacks
DoS and DDoS
Eavesdropping
Impersonation/Masquerading
Replay Attacks
Modification Attacks
Address Resolution Protocol Spoofing
DNS Poisoning, Spoofing, High jacking
Hyperlink Spoofing

## Slide 42: Summary
Remote access security management requires security systems to address the hardware and software components
Maintaining control over communication pathways is essential to supporting CIA for network, voice, and other forms of communications
Tunneling
VLAN
NAT
Switching technologies
WAN link technologies
Virtualizations
Internet-based email
Fax and voice security
Types of attacks